## Slide 1: Sensing and timing at Honeywell
Neal SOlmeyer
  Staff scientist, advanced sensors and microsystems Plymouth, MN
  Robert Compton, josh dorr, chad Fertig, Chad hoyt, sally-ann keyes, neil krugger, karl nelson, matthew puckett
This research was developed with funding from the Defense Advanced Research Projects Agency (DARPA)
The views, opinions and/or findings expressed are those of the author and should not be interpreted as representing the official views or policies of the Department of Defense or the U.S. Government.

## Slide 2
PhD. Penn State 2013 : Measurement of electric dipole moment of the electron
Army Research Laboratory, Adelphi MD, 2013 – 2017: Quantum communication, and sensing with Rydberg atoms
MITRE 2017-2018: consulting government on quantum and sensing technology

## Slide 3: Quantum sensors: atoms, laser light, & quantum states
  Accelerometers (gravimeters)
  Gyroscope (rotation)
  Magnetometer
  Clock (passage of time)
  Time transfer
Atoms and laser light can provide high sensitivity
Position, navigation, and timing

## Slide 4: Light Interferometer
To make an atom interferometer, we need to make the atoms do the same
acceleration or rotation
Light in two different paths
Area between the paths matters
Rotation sensor: pattern changes if there is rotation
By Stigmatella aurantiaca - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=25125975
Notes: Note: this is not a Honeywell-proprietary RLG picture (obtained from web)

## Slide 5: Ring laser gyroscope
First level of text, Arial Bold 24pt
  Second level of text, Arial 24pt
    Third level of text, bullet, Arial 20pt
Role of phase in RLG parallels some atomic sensors
  Two counter-propagating laser paths
  Fringe pattern tracks rotation
  Phase shift proportional to enclosed area
Notes: RLG images found in online search

## Slide 6: Resonator Fibre Optic Gyroscope
RFOG is a game changer for Inertial Navigation
Description – Revolutionary optical technology that combines advantages of ring laser (RLG) and fibre optic gyros (FOG) to provide a new highly scalable type of optical gyroscope that enables new trades between performance/size
Differentiation/Advantage – Low-cost & reduced SWaP architecture. Low loss hollow-core fibre. Chip-scale photonics and light sources.
Product Relevance – Commercial: Designs for extremely good performance in very low SWaP

## Slide 7: Optical Waveguide Laser Gyroscope (OWL-G)
Another low SWaP+C approach to GPS challenged navigation
Description – Brillouin scattering in optical resonators can generate extremely narrow linewidth lasers, which can be applied to optical gyroscopes
Differentiation/Advantage – monolithic chip-scale Brillouin laser gyroscopes can achieve lower SWaP than fiber gyros while achieving comparable levels of sensitivity and extreme robustness
Product Relevance – low SWaP gyros can be mounted on lightweight aircraft and projectiles
CW Laser
Phase Mod
SOA
CW Laser
Phase Mod
SOA
CW Laser
PhaseMod
SOA
Laser chip
Low loss waveguide on chip
Notes: scale factor of 152 Hz per degree per second
More on this kind of laser, SBS, later

## Slide 8: Sensor Variation
Histogram of variation in crystal frequency
Today’s sensors: Variation between parts
  Size, shape
  Composition
  Resonance frequency
  Most companies have “six-sigma” programs to address this variation
  Example: Ring-laser Gyro (RLG) measures rotation; area matters
  Example: Quartz oscillator measures time, but every crystal is different
Atom sensors: Every atom is the same
RLG: any variation in size changes its response to rotation
Notes: Sources: RLG diagram—used on 100s of sites on the web, origin unclear. Possibly Boeing aircraft manuals
RLG picture: from Wired Magazine, with credit to Honeywell in the caption

## Slide 9: Quantum sensors
Atomic states (phase) can be exquisitely sensitive
Atomic states
Laser light
microwave
transition
Energy
Superposition is particularly
sensitive: frequency changes (clock)
Atomic, laser and exclusively quantum-based sensors
Notes: To see how phase can lead to sensitive measurements, let’s look at a gyroscope like Honeywell’s, in production for decades

## Slide 10: How Cold are “Cold Atoms”?
3,000,000 K
30,000 K
300 K
3 K
0.03 K
3 µK
30 nK
Sun’s core
Sun’s photosphere
Life
Coldest naturally occurring temperature (deep space)
Coldest refrigerator (dilution fridge)
Laser cooling
Specialized laser cooling techniques
evaporative cooling
velocity selection
300 µK

## Slide 11: Atomic Interferometers
40 velocity recoils
(a)
(b)
Low SWaP+C approach to GPS challenged navigation
Atomic Sagnac interferometer exploits wave-like nature of cold atoms
Ultracold atoms manipulated by lasers & lattices can maximize accelerometer stability
Notes: 10 uK -> nK

## Slide 12: Atomic Interferometers
Overlapping optical lattices
-24 16 -8 0 8 16 24
∆f (recoils)
0
2 vr
4 vr
-2 vr
-4 vr
10
0
-10
-20
-30
Energy (recoils)
Bragg
Bloch
Bloch
Atom Interferometers with Scalable Enclosed Area
Müller Chiow, Herrmann, and Chu, Phys. Rev. Lett. 102, 240403 (2009)
Overlapping optical lattices
  Accelerate both halves of interferometer in opposite directions
  First demonstrated by Berkeley group (Bragg-Bloch-Bragg)

## Slide 13: Numerical simulations
+4 vr
- 4 vr
7x Bloch
Accelerate
Bragg
π/2
7x Bloch
Decelerate
7x Bloch
Accelerate
7x Bloch
Decelerate
Bragg
π/2
Bragg π
8 photon Bragg beamsplitter + 28 photon Bloch = 36 photon interferometer
Simplified Hamiltonian with 40 momentum states, adiabatic elimination of excited state
Temperature included by Monte Carlo average over Boltzmann distribution of atom velocities
Capability for Gauss-Markov treatment laser RIN and phase noise (not included below)

## Slide 14: Temperature considerations
Bragg beamsplitter efficiency strongly sensitive to temperture
13
8 photon Bragg beamsplitter plus
7 Bloch oscillations each path
= 36 photon maximum separation
Previous Bragg/Bloch data
Contrast > 15%
Numerical simulations vs temperature

## Slide 15: Gravitational Anomaly-Aided Navigation
Gravitational anomalies are caused by density variation in the Earth’s crust
Compare gravity measurement to an a priori gravity map for a position update
Similar to terrain-aided navigation
Longitude [deg]
Latitude [deg]
Anomaly [uG]
Gravitational Anomaly Map [uG]
Corresponding Google Earth Map
France
Spain
UK
Ireland

## Slide 16: Approach
Develop simulation for ship use-case
Simulate strapdown IMU aided with high quality vertical accelerometer
Simplification due to sea level altitude
Implemented necessary components for simulation
  Sensor data generation
  Strapdown navigation
  Strapdown navigation error model
  Particle filter with gravitational anomaly measurement and map update
  Filters for comparison (EKF and PF with position measurement and direct anomaly measurement)
Conduct trade study with simulation
Vary characteristics of system components
Vary initial conditions
Strapdown Navigation
Particle Filter
Sensor Data Generation
Sensor Data
Navigation Solution
Nav and Sensor Error Estimates
Trajectory
Error Model
Nav Solution, Sensor Data, Error Model
Gravitational Anomaly Map
Block Diagram of Current Simulation

## Slide 17: Simulation Setup and Example result
Trajectory details
    25 m/s (~50 knots)
    110.5 km (68.7 miles), 1hr 13min
    Constant sea level altitude
    Constant velocity and heading, no wave motion
    Trajectory covers region with strong East and North gradients
Filter details
    IMU errors consistent with HG9900
    Initial condition errors under 1km and 0.5 m/s in N and E directions
    Map uncertainty captured in filter tuning, but no map errors in the simulation
    Attitude error impact on gravity measurement not considered, negligible for this choice of trajectory
Start
Stop

## Slide 18: Example Result Details
Convergence associated with features on the map
0
4400
1000
2900
2000
    Vertical accel: 1 ug bias and -1 ppm scale factor for net 2 ug error
    Vertical accel: VRW 1.25e-3 ft/s/rt(hr) (1/2 Q-Flex VRW)
    Map error and unmodeled anomaly error uncertainty of 0.5ug
Distance (a.u.)
Distance (a.u.)

## Slide 19: Magnetic Anomaly aided navigation
Magnetic anomaly signal degraded at high altitudes, but applications remain
Proof of concept demonstrated by Air Force Institute of Technology
Miniature atomic magnetometers for scalar measurements are commercially available
Vector and gradient sensing may help to distinguish cabin noise from anomaly signal
200 km
120 km
Altitude = 500 m
Altitude = 3500 m
Altitude = 10500 m
Absolute positioning using the earth’s magnetic anomaly field Canciani and Raquet, J. Inst. Nav. 63, 111 (2016)

## Slide 20: Unshielded Vector atomic magnetometer
Measured magnetic noise higher than desired, but sufficient for magnetic anomaly nav
Noise is nearly identical (except for low frequency and 60 Hz components), likely coming from the heater current or magnetic coils in the setup
Improving the setup could reduce magnetic noise below expected sensitivity, improvements may include
  Improved heater using high frequency AC heating current
  Lower noise current source for nulling coils
  Sensing thermistor resistance using AC excitation current
  Low noise frequency generator for B-field modulation

## Slide 21: Precision timing: atomic clocks
Portable, optical atomic clock: orders of magnitude increased performance
Notes: Courtesy ASM group

## Slide 22: Miniature atomic Clocks
Chip scale atomic clock
DARPA CSAC, Army
Cold atom microwave clock
DARPA IMPACT, ACES
Two-photon rubidium optical clock
AFRL L-ROCK
Strontium optical lattice clock
DARPA A-PhI
Precision timing for GPS challenged environments
Chip-scale atomic clock
Optical grating for Magneto-optical trapping beams (DARPA ACES)

## Slide 23: Overview of Atomic Frequency Standard
+
Pre-cooled atoms allow for long Ramsey times
1. Cooling and trapping 87Rb from vapor
2. State preparation
3. Microwave spectroscopy
4. Fluorescence readout
5. Feedback to local oscillator
10 microK (10 millionths of a degree above absolute 0)
Notes: We are 30 million times hotter than these atoms
Sun surface is only 100 times hotter than us; hottest part is only 10,000x hotter

## Slide 24: Portable GPS-quality timekeeping (COASTER)
Low SWaP, long-term timing accuracy, without GPS
Description – combining proven cold atom clock physics with miniature microwave and optical components to realize ultra-stable atomic timekeeping with game-changing low SWaP
Differentiation/Advantage – laser cooled atoms promise 1000x increase in accuracy as compared to state of the art (CSAC), esp. over large temperature excursions.
Product Relevance – GPS Anti-jam/Anti-spoof, secure comms, direct code acq. in military and commercial markets.
Initial testing to metrics.
Averaging time [s]
100
104
Allan deviation [frac frequency]

## Slide 25: Ultra-cold atoms with waveguide structures
Photonic integrated circuits (PICs)
  Patterned waveguides
  Gratings that couple guided modes to free space
Low SWaP physics package
  B-field coils
  UHV chamber
  RF interrogation & detection
PICs promise significantly decreased size and weight
4 cm

## Slide 26: Optical lattice clock
Relative frequency instabilities of 3.2 x 10-19 achieved (NIST, Yb)
Ultra-stable continuous-wave laser
Ultra-narrow (doubly forbidden) atomic transition
Uses atomically stabilized laser to stabilize a frequency comb for clock output
Takes advantage of inherently stable optical transition:
instability
Notes: Challenge: achieve potential performance levels promised by lattice clocks in a low-SWaP architecture
Solution: PICs from previous slide and waveguide SBS lasers

## Slide 27: Integrated SBS laser
SBS lasers could enable next generation of chip-scale optical clocks
Gundavarapu et al., “Sub-hertz fundamental linewidth photonic integrated Brillouin laser,” Nature Photonics, 13, 60-67 (2019)
Stimulated Brillouin scattering process
  Waveguide architecture
  Process narrows laser linewidth

## Slide 28: Timing with entangled photons
Entangled photons could sync. distant satellites to <1ps.
“2002” entangled bi-photon states are produced by pumping a nonlinear crystal.
The condition of equal path time is reflected in a dramatic change in the coincidence statistics at the detectors.
Absolute ranging is not required for synchronizing the two clocks.
Enabling technologies:
  Robust entangled bi-photon source (lasers)
  Miniature optics

## Slide 29: Computing: Honeywell Quantum solutions
Honeywell has significant efforts in quantum-based technology
Current Offerings
Consulting & Design of Experiment
Engineering & Development
Quantum System Utilization (2019)
System architecture
Novel gate schemes
Application design
Components & subsystems
Cryogenic & vacuum systems
Control systems
Custom QIS test beds
Best-in-class computational capability
Chief Commercial Officer: Justin Ging
justin.ging@honeywell.com
Quantum Computing
Trapped-ion Qubit Technology

## Slide 30: Quantum sensors: enabling technologies
Low loss optical waveguides, extending into blue, UV
RF/microwave engineering
Lasers
    Integrated in active structures
    Stable over T in power and frequency
    New colours (e.g. UV)
Single and entangled photon sources
Optical fibers in blue/UV
Atomic sources
    Low generating power and small size
    Stable over T
UHV technology
Miniature optics
    Photonic chip interconnects
    Free-space and fibre coupling
Active Honeywell development in these areas

## Slide 31
Non-GPS navigation
Survey of quantum technologies
Future quantum technologies
Timing & synchronization
3P0
1S0
1P1
698 nm
Hosten, et al., Nature
529 505 (2016)
Komar, et al., PRL 117 060506 (2016)
Inertial