## Slide 1: Building Trees and Hacking Communications – QIS at MITRE
Yaakov S. Weinstein
Group Leader: Physical Sciences, Nanosystems, and Quantum Group
The MITRE Corp.
weinstein@mitre.org

## Slide 2: MITRE
At MITRE, we solve problems for a safer world.
Through our federally funded R&D centers and public-private partnerships, we work across government to tackle challenges to the safety, stability, and well-being of our nation.

## Slide 3: MITRE
At MITRE, we solve problems for a safer world.
Through our federally funded R&D centers and public-private partnerships, we work across government to tackle challenges to the safety, stability, and well-being of our nation.

## Slide 4: Physical Sciences, Nanosystems, and Quantum Group
The MITRE Physical Sciences, Nanosystems, and Quantum Group brings physics and chemistry expertise to bear on a wide range of critical sponsor challenges:
Quantum technologies: experimental and theoretical efforts and analysis in quantum sensing, communications and networking, and computation
Nano-based, atomic and other novel sensors: hypoglycemia and bacterial detection, nitrogen vacancies, chemical detection, atomic gravimeters, Rydberg antennas, atomic IMUs, atomic clocks
Material Science: armor, material hardening, nano-materials, high-temperature superconductors, desalination
Nuclear effects: directed energy and EMP analysis and modelling, communications in nuclear environment
Optics and Electromagnetics: super-resolution, structured beams, opto-mechanics, laser detection and identification
Start small, think big!

## Slide 5: Tree Clusters

## Slide 6: What is a Cluster-State?
or
Persistency: Number of measurements needed to dis-entangle state
z-measurement on first qubit
n = 4 state
persistency
or
1
n/2
Vertices are physical “qubits”
Edges represent the presence of entanglement between connecting “qubits”
Cluster states exhibit a persistent type of entanglement…

## Slide 7: What is a Cluster-State?
a
A cluster state can be constructed by applying the operator between neighbor qubits. With the qubits initially in the state:
How do you construct a cluster state?
Neighborhood of a
is characterized by a set of eigenvalue equations:
where N(a) is the neighborhood of a.
Now, measurement on any qubit may affect the state of the qubits in its neighborhood!
These are stabilizer states that play an important role in Quantum Error Correction and other Quantum Computing protocols…

## Slide 8: Cluster-Based Quantum Computation
Input: build 2-D cluster state by rotating all qubits into the state and applying between nearest neighbor qubits
Algorithm implementation: single-qubit measurements in the x-y plane. Previous measurement and angle of measurement axis determines gate
Output: Measure final column of qubits and perform required single-qubit corrections
Vertices are physical “qubits”
Edges represent the presence of entanglement between connecting “qubits”
Measure qubit in appropriate basis
z-measurement
y-measurement
Effect of measurements on cluster states
x-measurement

## Slide 9: Loss Resistant Cluster States
Tree clusters are especially useful for cluster state quantum computation because they are “loss-resistant”
A {2,2} tree cluster state:
Two initial branches each having two sub-branches
If this qubit is lost, we can still perform z-measurement by successfully measuring either of the branches such as shown here:
This is because the cluster state is a +1 eigenvector of the above- mentioned eigenvalue equation:
Z
Z
X

## Slide 10: Cluster Equivalences
We introduce an alternate way of constructing small tree clusters:
This method is more efficient than previous methods
It transforms chain clusters (a cluster state whose qubits are laid out in one dimension) to tree clusters without the need to add more qubits
We utilize local complementation: the fact that certain graphs are transformed into each other simply by applying single qubit rotations
Local complementation can be used to transform a cluster chain into a box (thus extending the qubits into a second dimension):
Where a qubit marked red indicates the application of a Hadamard gate:
Step 1:
Step 2:
Step 3:
Result

## Slide 11: Tree Cluster Construction
Construction of {2,2} tree cluster from chain cluster
Where a qubit marked red indicates the application of a Hadamard gate and one marked blue indicates a z-basis measurement

## Slide 12: Tree Cluster Construction
Construction of {2,3} tree cluster from chain cluster
Where a qubit marked red indicates the application of a Hadamard gate and one marked blue indicates a z-basis measurement

## Slide 13: Quantum Hacking

## Slide 14: Imperfect QKD creates vulnerabilities
Transmitter
Alice
Receiver
Bob
Quantum/Classical
Boundary
Quantum System
KEY
KEY
*
Classical Side Channel
Measurement Side Channel
Quantum State Imperfection
Information Leakage
Information can be extracted by an adversary (Eve) via multiple possible exploits
Alice
Bob
U
Eve
Quantum State Imperfection
KEY
KEY
*
Alice
Bob
KEY
KEY
*
Measurement Side Channel
Eve
Vulnerabilities via:
Imperfections in sender (Alice) or receiver (Bob) that can be actively probed or passively measured
Imperfections in channel encoding that create measurable side-channels (e.g. flashback)
Hardware exposure that could be actively controlled or manipulated by Eve
Passive attacks: Eve looks for leaked information that she can passively measure without revealing her presence
Active attacks: Eve manipulates the signal, actively probes Alice or Bob’s system through the channel, or even tries to remotely control some aspect of Alice/Bob’s system

## Slide 15: Sample list of known QKD attack vectors
Attack | Target Component | Tested System | Source
Backflash Attack | Single-Photon Detectors | ID Quantique, research system | Light: Science & Appls. 6, e16261 (2017) IEEE The Bridge 114, 18-29 (2018) Optics Express 26, 21020 (2018)
Photon Number Splitting (PNS) | Optical pulse source in Alice | (theory) | Phys. Rev. A 51, 1863 (1995) New J. Phys. 4, 44 (2002)
Inter-symbol Interference | Intensity Modulator in Alice | research system | NPJ Quantum Information 4, 8 (2018)
Pulse Energy Calibration | Classical Watchdog Detector | ID Quantique | Phys. Rev. A 91, 032326 (2015)
Wavelength-selected PNS | Intensity Modulator | (theory) | Phys. Rev. A 86, 032310 (2012)
Laser Damage | Multiple, Detector | ID Quantique, research system | Phys. Rev. Lett. 112, 070503 (2014) Phys. Rev. A 94, 030302 (2016)
Spatial Efficiency Mismatch | Receiver Optics | research system | Phys. Rev. A 91, 062301 (2015) IEEE J. Sel. Top. Quantum Electron. 21, 187 (2015)
Trojan-horse | Phase Modulator in Alice/Bob | SeQureNet, ID Quantique | IEEE J. Sel. Top. Quantum Electron. 21, 168 (2015) New J. Phys. 16, 123030 (2014) Sci. Rep. 7, 8403 (2017)
Detector control | Single-Photon Detector | ID Quantique, MagiQ, research system | New J. Phys. 11, 065003 (2009) Nat. Photonics 4, 686-689 (2010) Nat. Commun. 2, 349 (2011)
Deadtime | Single-Photon Detector | research system | New J. Phys. 13, 073024 (2011)
Multi-wavelength | Beamsplitter | research system | Phys. Rev. A 84, 062308 (2011)
Detector mismatch via channel miscalibration | Single-Photon Detector | ID Quantique | Phys. Rev. Lett. 107, 110501 (2011)

## Slide 16: Backflash from imperfect detectors
Most single photon detectors operate via photo-electric effect, where absorbed photon produces an electron-hole pair multiplied by a large gain to create many pairs
Some of the many electron-hole pairs recombine, creating a flash of light that may leak into the channel
The backflash propagates through the detection optics, carrying information about which qubit state was detected
Countermeasure: Prevent backflash from re-entering the channel e.g. via filters and a circulator

## Slide 17: Photon number splitting attack
High quality single photon sources are currently difficult to produce, so weak coherent pulses are often used instead
Imperfect sources inevitably lead to pulses with multiple photons or qubit copies
Eve can extract this copied information by discriminating based on pulse photon number
Countermeasure: Random ‘decoy state’ pulses at different intensities to probe channel for PNS attacks
"Quantum cryptography with coherent states," Phys. Rev. A 51, 1863 (1995).
"Quantum key distribution with realistic states: photon-number statistics in the photon-number splitting attack," New J. Phys. 4, 44 (2002).
"Quantum Key Distribution with High Loss: Toward Global Secure Communication," Phys. Rev. Lett. 91, 057901 (2003).

## Slide 18: Trojan horse attacks
Trojan horse attacks are active attacks on Alice and/or Bob through the quantum channel
Eve gains information by injecting light into Alice/Bob’s system and looks for state dependent information that is reflected back
Known vulnerabilities include reflections from phase modulators in Alice and Bob, or remote detector control in Bob
Countermeasures: Strong modal and temporal filtering and active auxiliary channel monitoring at Alice and Bob
"Trojan-horse attacks on quantum-key-distribution systems," Phys. Rev. A 73, 022320 (2006)
"Trojan-horse attacks threaten the security of practical quantum cryptography," New J. Phys. 16, 123030 (2014)
"Attacks exploiting deviation of mean photon number in quantum key distribution and coin tossing," Phys. Rev. A 91, 032326 (2015)
"Practical Security Bounds Against the Trojan-Horse Attack in Quantum Key Distribution," Phys. Rev. X 5, 031030 (2015)
"Risk Analysis of Trojan-Horse Attacks on Practical Quantum Key Distribution Systems," IEEE J. Sel. Top. Quantum Electron. 21, 168–177 (2015)
"Invisible Trojan-horse attack," Scientific Reports 7, 8403 (2017)

## Slide 19: Current Areas of Interest
Quantum Computer Metrics
  Determine utility of different metrics
  Formulate new and/or modify current ones
Quantum Key Distribution (QKD) and Hacking
  Identify new hacks and vulnerabilities in QKD systems
    Backflash from single photon detectors
  Layering of QKD with classical encryption protocols
  Continuous variable QKD
Quantum Networks
Quantum algorithms especially for Quantum Machine Learning and Graphs
  Resource requirements
  Improvement over classical
Atomic Sensors
  Quantum antennas
  Squeezed light
Quantum Annealers

## Slide 20
Carl Giller
Kathy Huynh
Jim Klemic
Bob Latham
Edlyn Levine
Steve Pappas
Brandon Rodenburg
Bonnie Schmittberger
Yaakov Weinstein
material science, analytical chem
mass spectrometry, analytical chem
nanotechnology, MEMS, c-WMD
Directed energy, metamaterials
Nuclear effects, HANE, plasmas
Quantum optics, quantum information optical physics
Atomic sensors, quantum optics
Exp. quantum info, modeling & sims
Group Leader
McLean Component
Bedford Component
Princeton Component
Charlie Fancher
Atomic sensors, quantum optics
PSN&Q Group